## Slide 1
The Smart Attic Pulley: Thermal Depth Sensor
A simple fixed pulley turns invisible attic heat loss into an actionable insight
JASON Autonomous Agent – Concept Engineering & Design Deck

## Slide 2
Executive Summary
• Low-cost, gravity-fed device for measuring insulation depth (d) using a fixed pulley and string.
• Dual temperature sensing: attic side (T_attic) and ceiling side (T_ceiling).
• App computes R-value estimate and heat-loss rate; quantifies £ and CO2 impact.
• Clear guidance: “Add ~15 cm insulation to reach R_target and stop paying for heat leakage.”
d

## Slide 3
The Invisible Problem: Heat Loss
• Homeowners lack tangible feedback about attic insulation performance.
• Thermal cameras provide snapshots; not a persistent, quantitative meter.
• Result: Under-insulated attics, higher bills, and avoidable CO2 emissions.

## Slide 4
The Drastic Change: Smart Attic Pulley
“Thermal Depth Sensor” hung from a joist; drop weight to touch insulation, measure depth d.
d
Human-Centered Insight
- Depth “d” correlates directly with thermal resistance.
- Turning a hidden variable into a tactile, repeatable measurement.
Smart Feedback Loop
- BLE to phone or hub; immediate R-value and heat loss estimate.
- Actionable: cost and CO2 per month with upgrade recommendation.

## Slide 5
Simple Machine: Fixed Pulley Mechanism
• Pulley + string/tape measure; weight lowers to insulation surface.
• Measure “d” via tape encoder or hall-effect ticks on drum.
• Re-zero on retraction for drift robustness.
d

## Slide 6
Sensing: T_attic and T_ceiling
• Dual thermistors/IC sensors (±0.2°C typical) for attic and ceiling surfaces.
• Optional IR spot sensor for ceiling gypsum surface temperature.
• Synchronized sampling during depth measurement to capture ΔT.

## Slide 7
Data Path & Connectivity
• Device MCU aggregates d, T_attic, T_ceiling; computes preliminary features.
• BLE GATT profile to mobile app/home hub (secure pairing).
• Edge storage for offline sessions; batch upload when connected.
BLE Payload (example)
- d_mm, T_attic_C, T_ceiling_C, timestamp_ms, battery_v
- flags: calibration_ok, contact_detected, sensor_ok

## Slide 8
Physics Model (Intuition)
• Insulation R-value scales with depth: R_insulation ≈ r_per_cm × d_cm.
• ΔT = T_attic − T_ceiling drives conductive flux through insulation.
• Heat flux q″ ≈ ΔT / R_total (simplified, steady-state).
R_total includes insulation plus framing/air films; app uses calibrated defaults adjusted by d and ΔT.

## Slide 9
From Measurement to Decision
• Estimate R_current from d and ΔT (with calibrated material constants).
• Target R_target based on climate zone and building code guidance.
• Compute monthly energy loss and £ / CO2; recommend added insulation thickness.

## Slide 10
Immediate Fact: What You’re Losing
• “Your attic is losing £X (Y kg CO2) / month.”
• “Add 15 cm to reach R_target; estimated payback: Z months.”
• Confidence indicator and measurement quality score.

## Slide 11
UX Flow
• Hang device on joist → Drop weight → Contact detect (soft).
• Device records d and T’s → Sends to app → Computes R and savings.
• App stores trend; suggests follow-up after upgrade.

## Slide 12
Mechanical Design Overview
• Enclosure with pulley drum, encoder wheel, thermistor probes, battery.
• Drop-weight with soft foot for insulation contact.
• String path guide; lock/retract latch.
Materials
- ABS/PC housing, stainless axle, low-stretch string/tape
- NEMA 1 flame rating; IP20 (attic dry enclosures)

## Slide 13
Electronics & Power
• MCU (BLE SoC), dual temp sensors, encoder input, coin cell / AA pack.
• Low-power sleep; wake on movement/contact.
• Optional rechargeable Li-ion with USB-C.

## Slide 14
Firmware State Machine
• IDLE → MEASURE (depth+temps) → TRANSMIT → SLEEP.
• Calibration routine for zero and encoder scale.
• Error handling: contact fail, sensor out-of-range.

## Slide 15
BLE GATT (Example)
• Service: 0xFFF0; Chars: d_mm, T_attic, T_ceiling, quality, battery_v.
• Notify on measurement complete; Read historical summary.
• Secure bonding; privacy-preserving identifiers.

## Slide 16
Mobile App: Information Architecture
• Capture screen: Live measurement + quality score.
• Insight screen: R_current vs R_target, £/CO2 per month.
• Action screen: “Add 15 cm” → local suppliers/DIY guidance.

## Slide 17
Installation & Safety
• Hang from joist; avoid electrical fixtures; PPE for attic dust.
• Contact foot is soft; no puncture of vapor barrier.
• RoHS/REACH compliance; battery transport guidance.

## Slide 18
Indicative BOM & Cost
• MCU+BLE: £3–6; Temp sensors: £1–3; Encoder: £1–2; Plastics+HW: £2–4.
• Assembly/test: £1–3; Battery: £1–3 → COGS target: £10–18.
• Retail target: £39–59; Payback typically < 6 months.

## Slide 19
Environmental Impact
• Distributed, persistent reduction of residential heat loss.
• Simple measurement → sustained behavioral change.
• Scalable via DIY channels and energy utility programs.

## Slide 20
Design Process & Next Steps
• Sketches → CAD → 3D print → Bench test sensors → Attic pilot.
• Calibrate physics model; validate R and savings accuracy.
• Finalize BLE/app UX; certifications; launch beta.